## Slide 1: Lectures for 2nd Edition
Note: these lectures are often supplemented with other materials and also problems from the text worked out on the blackboard. You’ll want to customize these lectures for your class. The student audience for these lectures have had assembly language programming and exposure to logic design

## Slide 2: Chapter 1

## Slide 3: Introduction
Rapidly changing field:
  vacuum tube -> transistor -> IC -> VLSI (see section 1.4)
  doubling every 1.5 years: memory capacity processor speed (Due to advances in technology and organization)
Things you’ll be learning:
  how computers work, a basic foundation
  how to analyze their performance (or how not to!)
  issues affecting modern processors (caches, pipelines)
Why learn this stuff?
  you want to call yourself a “computer scientist”
  you want to build software people use (need performance)
  you need to make a purchasing decision or offer “expert” advice

## Slide 4: What is a computer?
Components:
  input (mouse, keyboard)
  output (display, printer)
  memory (disk drives, DRAM, SRAM, CD)
  network
Our primary focus: the processor (datapath and control)
  implemented using millions of transistors
  Impossible to understand by looking at each transistor
  We need...

## Slide 5: Abstraction
Delving into the depths reveals more information
An abstraction omits unneeded detail, helps us cope with complexity What are some of the details that appear in these familiar abstractions?

## Slide 6: Instruction Set Architecture
A very important abstraction
  interface between hardware and low-level software
  standardizes instructions, machine language bit patterns, etc.
  advantage: different implementations of the same architecture
  disadvantage: sometimes prevents using new innovations True or False: Binary compatibility is extraordinarily important?
Modern instruction set architectures:
  80x86/Pentium/K6, PowerPC, DEC Alpha, MIPS, SPARC, HP

## Slide 7: Where we are headed
Performance issues (Chapter 2) vocabulary and motivation
A specific instruction set architecture (Chapter 3)
Arithmetic and how to build an ALU (Chapter 4)
Constructing a processor to execute our instructions (Chapter 5)
Pipelining to improve performance (Chapter 6)
Memory: caches and virtual memory (Chapter 7)
I/O (Chapter 8) Key to a good grade: reading the book!

## Slide 8: Evolução capacidade de memória

## Slide 9: Evolução do desempenho

## Slide 10: Chapter 2

## Slide 11: Performance
Measure, Report, and Summarize
Make intelligent choices
See through the marketing hype
Key to understanding underlying organizational motivation Why is some hardware better than others for different programs? What factors of system performance are hardware related? (e.g., Do we need a new machine, or a new operating system?) How does the machine's instruction set affect performance?

## Slide 12
Which of these airplanes has the best performance?
Airplane Passengers Range (mi) Speed (mph)
Boeing 737-100 101 630 598
Boeing 747 470 4150 610
BAC/Sud Concorde 132 4000 1350
Douglas DC-8-50 146 8720 544
How much faster is the Concorde compared to the 747?
How much bigger is the 747 than the Douglas DC-8?

## Slide 13: Computer Performance: TIME, TIME, TIME
Response Time (latency) — How long does it take for my job to run? — How long does it take to execute a job? — How long must I wait for the database query?
Throughput — How many jobs can the machine run at once? — What is the average execution rate? — How much work is getting done?
If we upgrade a machine with a new processor what do we increase?
If we add a new machine to the lab what do we increase?
Notes: Have them raise their hands when answering questions

## Slide 14: Execution Time
Elapsed Time
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program

## Slide 15: Book's Definition of Performance
For some program running on machine X, PerformanceX = 1 / Execution timeX
"X is n times faster than Y" PerformanceX / PerformanceY = n
Problem:
  machine A runs a program in 20 seconds
  machine B runs the same program in 25 seconds
  quanto mais rápida é a máquina A com relação à B?

## Slide 16: Clock Cycles
Instead of reporting execution time in seconds, we often use cycles
Clock “ticks” indicate when to start activities (one abstraction):
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec) A 200 Mhz. clock has a cycle time
clock rate = freqüência
cycle time = período
time

## Slide 17: How to Improve Performance
So, to improve performance (everything else being equal) you can either ________ the # of required cycles for a program, or ________ the clock cycle time or, said another way, ________ the clock rate.

## Slide 18: Fórmulas
tCPU = tCK * (Nº de períodos) = (Nº de períodos) / fCK

## Slide 19: How many cycles are required for a program?
Could assume that # of cycles = # of instructions
This assumption is incorrect, different instructions take different amounts of time on different machines. Why? hint: remember that these are machine instructions, not lines of C code
time
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...

## Slide 20: Different numbers of cycles for different instructions
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than accessing registers
Important point: changing the cycle time often changes the number of cycles required for various instructions (more later)
time

## Slide 21: Example (2.3, pag 60)
Our favorite program runs in 10 seconds on computer A, which has a 400 Mhz. clock. We are trying to help a computer designer build a new machine B, that will run this program in 6 seconds. The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program. What clock rate should we tell the designer to target?"
Don't Panic, can easily work this out from basic principles

## Slide 22: Now that we understand cycles
A given program will require
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocubulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  CPI (cycles per instruction) a floating point intensive application might have a higher CPI
  MIPS (millions of instructions per second) this would be higher for a program using simple instructions

## Slide 23: Performance
Performance is determined by execution time
Do any of the other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall: thinking one of the variables is indicative of performance when it really isn’t.

## Slide 24: CPI Example (2.3, pag 62)
Suppose we have two implementations of the same instruction set architecture (ISA). For some program, Machine A has a clock cycle time of 10 ns. and a CPI of 2.0 Machine B has a clock cycle time of 20 ns. and a CPI of 1.2 What machine is faster for this program, and by how much?
If two machines have the same ISA which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will always be identical?

## Slide 25: Fórmulas
tCPU = tCK * (Nº de períodos) = (Nº de períodos) / fCK
IC = Instruction Count = Nº total de instruções
tCPU = (Nº de períodos) / fCK = (IC * CPI) / fCK
Nº de períodos =
CPImédio =
IC =

## Slide 26: # of Instructions Example (pag 64)
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require one, two, and three cycles (respectively). The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C. Which sequence will be faster? How much? What is the CPI for each sequence?

## Slide 27: MIPS example
Two different compilers are being tested for a 100 MHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles (respectively). Both compilers are used to produce code for a large piece of software. The first compiler's code uses 5 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions. The second compiler's code uses 10 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?

## Slide 28: MIPS example (cont´d)
tCPU1 = (5*1+1*2+1*3) * 1E6 * 10 ns = 100 E-03 = 100 ms  mais rápido
tCPU2 = (10*1+1*2+1*3) * 1E6 * 10 ns = 150 E-03 = 150 ms
MIPS1 = (5+1+1) / 0.1 = 70 MIPS
MIPS2 = (10+1+1) / 0.15 = 12 / 0.15 = 80 MIPS  mais rápido
resultados conflitantes para um mesmo programa, em um mesmo computador
f=100 MHz  T = 10 ns

## Slide 29: MIPS
MIPS não é medida confiável de desempenho
Tentativas:
  MIPS de pico (pior ainda)
  MIPS relativo
  Máquina de referência mais usada é o VAX 780 (1 MIPS) VUP (VAX Unit of Performance)

## Slide 30: MFLOPS
Milhões de operações de ponto flutuante por segundo (+-*/ ex)
Problemas:
  depende do programa
  programa sem ponto flutuante  0 MFLOPS
  depende do conjunto de instruções (ex: divisão é uma instrução ou é uma sequencia de passos)
Alternativas:
  MFLOPS normalizado: peso diferenciado nas instruções na linguagem em alto nível (multiplicação mais complexo do que soma)

## Slide 31: Benchmarks
Performance best determined by running a real application
  Use programs typical of expected workload
  Or, typical of expected class of applications e.g., compilers/editors, scientific applications, graphics, etc.
Small benchmarks
  nice for architects and designers
  easy to standardize
  can be abused (opções especiais de compilação)
SPEC (System Performance Evaluation Cooperative)
  http://www.specbench.org/
  companies have agreed on a set of real program and inputs
  can still be abused (Intel’s “other” bug) (programa “otimizado” por compilador “especial” era errado !!!)
  valuable indicator of performance (and compiler technology)

## Slide 32: SPEC ‘89
Compiler “enhancements” and performance

## Slide 33: SPEC ‘95

## Slide 34: 2.5 Comparando benchmarks
Para eliminar “peso” de programas mais longos  normalização
Quando os tempos de execução são normalizados deve-se usar a média geométrica
Propriedade de MG
Atenção: MG não representa o tempo de execução (depende da distribuição estatística)

## Slide 35: SPEC ‘95
Does doubling the clock rate double the performance?
Can a machine with a slower clock rate have better performance?
Aumento de desempenho para o mesmo clock
tCPU = = (IC * CPI) / fCK
Taxa de ganho é menor do que a taxa de aumento do clock

## Slide 36: Exemplos de medidas
mostrar transparências SPEC

## Slide 37: Amdahl's Law
Execution Time After Improvement = Execution Time Unaffected +( Execution Time Affected / Amount of Improvement )
Example (2.7, pag 75): "Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?" How about making it 5 times faster?
Principle: Make the common case fast

## Slide 38: Example
Suppose we enhance a machine making all floating-point instructions run five times faster. If the execution time of some benchmark before the floating-point enhancement is 10 seconds, what will the speedup be if half of the 10 seconds is spent executing floating-point instructions?
We are looking for a benchmark to show off the new floating-point unit described above, and want the overall benchmark to show a speedup of 3. One benchmark we are considering runs for 100 seconds with the old floating-point hardware. How much of the execution time would floating-point instructions have to account for in this program in order to yield our desired speedup on this benchmark?

## Slide 39: Remember
Performance is specific to a particular program/s
  Total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance
You should not always believe everything you read! Read carefully! (see newspaper articles, e.g., Exercise 2.37)